## Slide 1: Decision Making Matrix
Taking a Close Look at Preliminary Ideas
Developed by Project Lead the Way

## Slide 2
Develop a Decision Matrix
A decision matrix is used to compare design solutions against one another, using specific criteria that are often based on project requirements.

## Slide 3: Decision-Matrix (Pugh’s method)
A weighted decision matrix

## Slide 4: Design Selection –Pugh’s Method
The method is an iterative evaluation that quickly identifies the strongest design solution.
Step 1 –Select the Criteria for Comparison
  The list of criteria must be developed from the customer needs and engineering specifications. All team members should contribute in making the list.

## Slide 5
Step 2 –Select the Design Solutions to be Compared
  The alternative design solutions should be those that proceed from the brainstorming.
Step 3 –Generate the Score
  A favorite design solution should be selected as a datum. All other designs are compared to it relative to each customer needs. For each comparison, the concept being evaluated is judged to be either better than (“+” score), about the same (“s” score), or worse than the datum (“-” score).
  Numeric scores can also be used.
Design Selection –Pugh’s Method

## Slide 6: Design Selection –Pugh’s Method
Step 4 –Compute the total score
  Three scores are tallied, the number of plus scores, the number of minus scores and the total.
  If most designs get the same score on a certain criterion, examine that criterion closely. More knowledge may have to be developed in the area of the criterion.

## Slide 10
Numeric Scores Can Be Used
A numeric scale can be developed to assign values for each criteria category.
Rank Scale
Question Scale

## Slide 11
Numeric Rankings
2
3
1
4
1
4
2
1
2
2
2
1
1
2
4
4
3
3
2
2
1
2
1
1
1
2
3
4
3
2
1
1
2
4
2
3
1
1
4
2
2
3
10
12
17
22
14
17

## Slide 12
Identifying Criteria
Cost
Reusability
Geometry
Connections
Cleanliness
Resilience
Testability

## Slide 13
Other Types of Criteria
Function
Product life span
Development time
Size
Material costs
Development costs
Manufacturing costs
Company standards
Manufacturing capabilities
Safety

## Slide 14
Design decisions should be based on analysis and logic; not personal opinion.
A decision matrix is a design tool that may be used multiple times throughout a design process.
The Right Decision