## Slide 1: Atmospheric Chemistry Module

## Slide 2: The Research
The Cavity Ring-Down Spectrometer (CRDS) uses lasers to analyze samples of atmospheric gases.
Gases can be identified from the CRDS data.

## Slide 4
I0
Intensity (mA)
I0/e
t
t0
Cavity with absorber
Empty cavity
Time (microseconds)
Compound | s (cm2/molecule)
SO2 | 6.572659 x 10-19
NO | 2.683 x 10-17
N2O | 1.47 x 10-19
CO2 | 1.137 x 10-16
O3 | 3.56 x 10-21
H2O | 2.0 x 10-24
CH4 | 1.90 x 10-17
CO | 2.15 x 10-17
SF6 | 4.511 x 10-17
NO2 | 6.11 x 10-19
CFCs | 5.23 x 10-22
a = absorption coefficient in cm-1
s = absorption cross-section in cm2/molecule
N = concentration in molecules/cm3
d = length of the cavity = 1 cm
c = speed of light = 3.0 x 108 m/s = 3 x 104 cm/ms
= time constant for cavity with absorber in ms
t0 = time constant for empty cavity in ms

## Slide 5: Planning
This project combines four classes: AP/IB Biology, AP/IB Chemistry, AP/IB Earth and Environmental Systems, AP/IB Physics.
Divide students into groups of 4 with one student from each class in the group.
  This can be used as the IB Group 4 Project.

## Slide 6: The Project
Video of Cavity Ring-Down Spectrometer
Analyze real research to determine the specific gases present in a sample of atmospheric gases

## Slide 7
Chart: Cavity Ring-Down Data for Gas A
I0
t = 13

## Slide 8: Calculation
s(1.44 x 1010 molecules/cm3) = (1cm/3x104cm/ms)[(1/ 13ms)-(1/40ms)]
= 1.2019 x 10-16 cm2/molecule
This most closely corresponds with
CO2.
Compound | s (cm2/molecule)
SO2 | 6.572659 x 10-19
NO | 2.683 x 10-17
N2O | 1.47 x 10-19
CO2 | 1.137 x 10-16
O3 | 3.56 x 10-21
H2O | 2.0 x 10-24
CH4 | 1.90 x 10-17
CO | 2.15 x 10-17
SF6 | 4.511 x 10-17
NO2 | 6.11 x 10-19
CFCs | 5.23 x 10-22

## Slide 9: The Project
Research emission sources of your specific gas
  Ours is CO2
Design an experiment to reduce your emissions of CO2
Implement the experiment over an 8 week period
Create a proposal for High Point City Council detailing ways to reduce CO2 emissions in the city
  $1 million budget
Multimedia presentations for city council members, school board members, and other officials

## Slide 10: Modifications
Eliminate the calculation portion by simply assigning a gas to each group.
Do the experiment with only one class.
Do the experiment entirely in class.
Give extra credit for the proposal portion.